## Slide 1
EXECUTIVE TECHNICAL PROGRESS REPORT | SEPTEMBER 2026
RoadSense: Multimodal Automotive ADAS Logger
Hardware-Synchronized Radar, Vision, GNSS & CAN Ingestion Cockpit for Vehicle Dynamics & Perception Research
77 GHz Radar 3.125 Mbps TI AWR1843BOOST mmWave raw point clouds & EKF tracks at 20 Hz
Camera2 Engine 1080p @ 30 FPS Hyperfocal infinity lock, tap AF/AE, autonomous Road AE
CANedge2 Bus 2x CAN / CAN-FD Autonomous 60s split MF4 staging, Wi-Fi sync & smart FIFO pruner
GNSS / GPS 1 Hz Fused + NMEA Nanosecond-indexed latitude, longitude, speed & heading track
Core Engineering Achievement to Date • Unified Cockpit: Single Android smartphone acts as an autonomous multi-sensor edge recorder. • Microsecond Alignment: Common monotonic time base eliminates cross-sensor clock drift. • Production Grade: Zero dropped radar packets, non-blocking Wi-Fi sync, and continuous diagnostics.
[ HARDWARE RIG PHOTO ] Vehicle Rig & Cockpit Mount Insert photo of test vehicle with bumper radar and windshield smartphone clamp.

## Slide 2
SYSTEM ARCHITECTURE
End-to-End Multimodal Data Pipeline
From physical vehicle hardware to Android edge ingestion and PC analytics
ROADSENSE ADAS
1. Sensor Layer Automotive Hardware
• TI AWR1843 Radar (77 GHz)
• Smartphone Camera2 Sensor
• CSS Electronics CANedge2
• Fused Multi-GNSS Constellation
2. Ingestion Engine Android Background Services
• 3.125 Mbps FTDI USB UART
• Non-blocking TextureView Preview
• Sequential HTTP REST / Wi-Fi AP
• Monotonic Clock: elapsedRealtimeNanos
3. Session Storage On-Device Monotonic Index
• session_timeline.csv (Unified Spine)
• radar_raw_stream.bin & frames.bin
• camera_video.mp4 & frames.csv
• can/*.MF4 (60s Split Chunks)
4. PC Analytics ADB Extraction & Visualization
• Automated sync_and_process_logs.bat
• Nearest-neighbor time interpolation
• Web-based BEV Radar/Video Player
• 7 Standalone diagnostic health tools
Deterministic Decoupling: Ingestion threads run on isolated IO and Default dispatchers to guarantee that heavy UI rendering or CAN HTTP downloads never block real-time 3.125 Mbps radar serial processing.

## Slide 3
CORE INNOVATION
Monotonic Cross-Sensor Nanosecond Synchronization
Solving physical clock domain jitter across Radar, Video, GNSS, and CAN
ROADSENSE ADAS
The Clock Domain Challenge in ADAS • Wall-Clock Flaws: System.currentTimeMillis() is prone to cellular NTP step adjustments, daylight savings shifts, and non-monotonic discontinuities. It CANNOT be used for sensor fusion. • The Monotonic Guarantee: RoadSense uses SystemClock.elapsedRealtimeNanos(). It ticks continuously from CPU boot, has microsecond resolution, and NEVER steps backwards. • Unified Spine: session_timeline.csv records every cross-sensor event with an exact nanosecond monotonic index: - [t0 + 35ms] RADAR_FRAME #1 (32 points, 2 tracks)
- [t0 + 40ms] CAMERA_FRAME #1 (PTS us -> Mono ns)
- [t0 + 90ms] GNSS_FIX #1 (Lat, Lon, Speed, Bearing)
- [t0 + 60s] CAN_MF4_CHUNK (00000041_00000051.MF4)
[ SYNC ALIGNMENT PLOT ] Timeline CSV Sync & Alignment Plot Insert plot or timeline diagram showing nanosecond nearest-neighbor interpolation between radar and camera frames.

## Slide 4
PERCEPTION SUBSYSTEM
TI mmWave Radar @ 3,125,000 Baud
Zero-loss high-speed USB serial UART driver, TLV parser, and EKF hardware tracking
ROADSENSE ADAS
ZERO-COPY RING BUFFER 3.125 Mbps UART Pipeline Custom FTDI/CDC serial driver configured for 3.125 Mbps. Handles sustained 15 MB/min binary bursts with zero dropped bytes or framing corruptions.
20 HZ POINT CLOUDS Real-Time TLV Packet Parser Decodes TI mmWave TLV binary streams in real time: Type 1 (Cartesian X, Y, Z + Doppler Velocity + SNR) and Type 7 (Hardware EKF Track IDs & Pos/Vel vectors).
100% BITSTREAM FIDELITY Dual Binary Session Logging Simultaneously writes raw UART byte streams (radar_raw_stream.bin) for replaying in TI mmWave Studio and structured frames (radar_frames.bin) for fast analytics.
Radar Driver Technical Specifications • Sensor Model: Texas Instruments AWR1843BOOST (77-81 GHz) • CLI Control Baud: 115,200 bps | Data Stream Baud: 3,125,000 bps • Frame Rate: 20 Hz (50 ms frame periodicity) • Max Range: 50.0 meters | Velocity Resolution: 0.15 m/s • Azimuth FOV: ±60° (120° total) | Elevation FOV: ±15°
[ RADAR BEV CANVAS SLOT ] Radar Bird's-Eye View (BEV) Display Insert screenshot of the real-time Radar Canvas showing point clusters and colored velocity tracks.

## Slide 5
VISION SUBSYSTEM
Camera2 Engine & Autonomous Road AE
Eliminating sky-bloom, windshield focus hunting, and preview touch glitches
ROADSENSE ADAS
ZERO-GLITCH LIFECYCLE Viewfinder Continuity • Problem: UI tab swipes previously triggered transient recomposition tearing down preview surfaces.
• Solution: Decoupled viewfinder lifecycle from compose gestures; surfaces remain pinned to Camera HAL session.
• Result: Smooth, flicker-free tab navigation.
AUTO-LOCK ON RECORD Hyperfocal Infinity Lock • Problem: Windshield rain, reflections, and dust trick AF into hunting and focusing on glass.
• Solution: Smart Infinity Focus locks lens distance (LENS_FOCUS_DISTANCE = 0.0f).
• Interactive Tap AF/AE: User tap targets license plates with dedicated yellow reticle overlay.
DUAL-ZONE PHOTOMETRICS Autonomous Road AE • Problem: Bright daylight sky overexposes and drives camera ISP to plunge road surface into darkness.
• Approach 3: 4 Hz non-blocking 32x24 thumbnail analyzer computes sky-to-road contrast ratio R.
• Dynamic State: When R >= 1.8x, locks AE metering to bottom 65% + adds EV boost.
Road AE Dynamic State Transitions • SKY_BLOOM (R >= 1.8x): Bottom 65% road metering + 0.5 EV boost (Status: • ROAD AE ☀️) • BALANCED (0.9x <= R < 1.8x): Full-frame matrix metering (Status: • ROAD AE) • NIGHT_TUNNEL (R < 0.9x): Sky rejection disabled to protect headlight visibility • TAP_LOCKED: User manual lock holds priority until [Reset Lock] is pressed.
[ CAMERA DECK SCREENSHOT ] Viewfinder UI with Road AE Badge Insert screenshot showing live camera preview with • ROAD AE ☀️ badge and focus controls.

## Slide 6
CAN SUBSYSTEM
CANedge2 Dual-Channel Ingestion & Smart Pruner
Autonomous Wi-Fi AP sync, 60s split MF4 handling, and single-connection protection
ROADSENSE ADAS
CANedge2 Autonomous Ingestion Engine • Cyclic 60s MF4 Splitting: CANedge2 continuously writes 1-minute split MF4 (MDF4) files over CAN1 (500 kbps) and CAN2 (CAN-FD). • 2-Folder Staging Pool (canedge_pool/): Maintains an active staging buffer of the two most recent folders, eliminating download bottlenecks during recording. • Single-Connection MCU Protection (Bug #10 Solved): CANedge's ESP32 web server crashes under concurrent polling. RoadSense enforces sequential non-blocking downloads with 1.5s backoffs. • Smart Auto-Pruner: Background FIFO cleans orphaned chunks while rescuing drive session files into permanent storage.
[ CANEDGE EXPLORER SCREENSHOT ] CANedge 3-Column File Explorer Deck Insert screenshot of the CANedge dashboard showing the nested directory tree and synchronized file indicators.

## Slide 7
COCKPIT UX & RELIABILITY
Cockpit UI Suite & Continuous Flight Recorder
6 dedicated telemetry tabs and dual-stream diagnostic logging
ROADSENSE ADAS
Multi-Tab Compose Cockpit Architecture • Radar Tab: Real-time BEV canvas, point cloud density, EKF track list, and CLI configuration terminal. • Side-by-Side (SBS) Tab: Synchronized dual-feed placing the 1080p camera viewfinder beside the 20 Hz Radar BEV display. • Camera Tab: Lens switching (Wide, Ultra-Wide), resolution/FPS controls, infinity lock, and Road AE controls. • CANedge Tab: Wi-Fi AP status, staging pool health, and OneDrive-style 3-column file manager. • Continuous Flight Recorder: Continuous app_system.log logs idle discovery and UI events; session_debug.log records active drives.
[ SBS COCKPIT SCREENSHOT ] Side-by-Side (SBS) Synchronized Cockpit Insert screenshot of the SBS Cockpit tab showing live camera preview and radar point cloud running concurrently.

## Slide 8
PIPELINE & TOOLING
PC Extraction & Offline Validation Tools
Automated ADB sync, web visualizer player, and 7 standalone health-check scripts
ROADSENSE ADAS
AUTOMATED ADB PIPELINE sync_and_process_sessions.py One-click extraction: pulls completed sessions from phone, validates file integrity, and compiles multimodal data into web visualizer JSON.
INTERACTIVE PLAYBACK Browser-Based Visualizer Full browser UI with synchronized video scrubbing, 20 Hz radar point clouds, ground-truth speed graphs, and telemetry overlays.
SESSION DIAGNOSTICS session_health_check.py Audits folder structures, checks cross-sensor timeline continuity, verifies MF4 byte strides, and flags missing frames or dropped packets.
MICROSECOND AUDITING audit_cross_sensor_sync.py Calculates cross-sensor latency offsets between radar frame headers and camera exposure PTS timestamps down to microsecond precision.
[ WEB VISUALIZER SCREENSHOT ] Web Visualizer Playback Deck Insert screenshot of the browser-based multimodal visualizer showing synced radar and video.

## Slide 9
FUTURE ROADMAP
The Next Frontier: Radar-Camera Sensor Fusion
Projecting metric 3D radar detections onto the 2D video viewfinder (FUSION_STEPS)
ROADSENSE ADAS
Phase 1: Spatial Calibration Immediate Priority
• Pinhole Intrinsics (K): Extracted via Camera2 API (fx, fy, cx, cy).
• 6-DOF Extrinsics [R | T]: Rigid rotation (pitch, yaw, roll) & translation offsets.
• Keystone HUD: Interactive on-screen sliders and +/- 0.1° nudge buttons.
• Target Pin & Snap: Drag floating radar reticle onto parked vehicle to auto-solve.
Phase 2: Viewfinder Fusion ADAS Overlay
• Doppler Point Overlay: Real-time 20 Hz projection colored by radial velocity (Cyan/Green/Red).
• 3D Bounding Boxes: Perspective cuboids anchored to ground plane (Z = 0).
• Telemetry Pill: Floating ID, distance, speed, and Time-to-Collision (TTC).
• FCW Warning: Visual border flash when TTC < 2.0 seconds.
Phase 3: Semantic AI Fusion Deep Association
• On-Device 2D Detection: Lightweight YOLOv8-nano running on NPU via TFLite.
• IoU & Mahalanobis Gating: Associating 2D vision boxes with 3D radar tracks.
• Complementary Advantage: Vision provides semantic class; Radar provides exact depth & speed.
Flat-Earth Road-Plane Anchor: Enforcing a ground-plane constraint (Z_road = 0) overcomes the coarse elevation resolution of standard mmWave radar, preventing objects from falsely floating in the sky.

## Slide 10
EXECUTIVE SUMMARY
Project Milestones, Quality Metrics & Next Steps
Consolidated deliverables, automated verification status, and upcoming roadmap
ROADSENSE ADAS
Subsystem / Feature | Engineering Status | Verified Performance Metric
TI mmWave Radar | Production Ready | 3.125 Mbps sustained; 0 dropped packets; 20 Hz
Monotonic Sync Spine | Production Ready | Microsecond alignment in session_timeline.csv
Camera2 Road AE & Focus | Production Ready | 4 Hz dual-zone photometric analysis; auto infinity
CANedge2 Ingestion | Production Ready | 2-folder pool; single-connection backoff; FIFO pruner
Continuous Flight Recorder | Production Ready | Continuous idle logging (app_system.log)
Automated JVM Testing | 100% Pass Rate | All unit tests clean; zero regression in master
Immediate Next Steps & Roadmap 1. Phase 1 Radar-Camera Calibration: Implement Keystone HUD with sliders for pitch/yaw and build the Target Pin & Snap solver for 60-second field setup. 2. Live Viewfinder Overlay (Phase 2): Render real-time Doppler color-coded radar points and 3D cuboids onto the active Camera2 TextureView. 3. Native Kotlin DBC Decoding: Extract vehicle speed and steering angle directly from CANedge MF4 files on the phone for ego-motion compensation. Questions & Technical Discussion

## Slide 11
ROADSENSE MOBILE ADAS DATA LOGGER SYNC • RECORD • VISUALIZE • ANALYZE
TI AWR1843BOOST 77 GHz mmWave Radar • Raw Point Clouds & Micro-Doppler Velocity • Hardware EKF Target Tracks & Clusters • Dual UART: 3.125 Mbps Data + 115.2 kbps CLI
[ RADAR BOARD ]
AWR1843BOOST
Antenna Array
High-Speed USB Serial UART (3.125 Mbps)
CSS Electronics CANedge2 (Dual-Channel CAN / CAN-FD)
[ CANedge2 HARDWARE ]
Dual DB9 Enclosure
SD Card Logging
OBD-II / Vehicle Powertrain Bus,
Cyclic 1-min MF4 Split Logging
2.4 GHz Wi-Fi AP
HTTP REST Sync
16:14 • RADAR 20.0 Hz CAM 30.0 fps GPS 1.0 Hz CPU 13% | BAT 55% 36.2°C
[ CAMERA FEED ]
1080p Viewfinder
• ROAD AE ☀️ Active
Hyperfocal Infinity
[ RADAR BEV SCOPE ]
• 60m Scope Rings
• Doppler Clusters
• Track IDs & TTC
Built-in Smartphone Sensors
Camera (Camera2 API) 1080p H.264 MP4 Stream with Nanosecond Frame Shutter Timestamps
GPS / GNSS (Location) 10 Hz NMEA Trajectory, Heading, Speed & Monotonic Fix Quality
ROADSENSE DATA LOGGER (Master Sync Engine)
Monotonic Timeline Master
(session_timeline.csv)
Continuous Flight Recorder
(app_system.log)
Synchronized Live BEV HUD
(20 Hz Side-by-Side)