## Slide 1
SPRINT 3 TECHNICAL HANDOVER
RoadSense: Week 3 Progress Inverse Perspective Mapping, Coordinate Decoupling & Multi-Sensor Hardening
PERCEPTION & IPM Inverse Perspective Mapping & 3D Vision Closed-form flat-earth raycasting (Z=0) running at 50+ FPS with YOLO26 + ByteTrack; non-destructive MCAP topic injection (/vision/geo_tracks) in Electric Magenta.
SPATIAL ALIGNMENT & SYNC IMU Auto-Leveling & Master Sync 1-tap gravity pitch sync, digital clamp spirit level, camera/radar yaw decoupling (Bug #25), and Master Timeline Synchronizer eliminating 2.16s video phase lead.
DEEP-TECH TOOLCHAIN Perfetto Tracing & Interactive HTML On-device Linux kernel scheduler tracing via ADB shell (<0.05ms app slice), standalone zero-dependency HTML audit reports with mouse-locked HUD, and 10,400 FPS conversion.
Bajaj Auto Ltd. • Advanced Perception and Telemetry
October 2026 • Sprint 3 Handover

## Slide 2
Sprint 3 Deliverables: From Optical IPM to Nanosecond Hardware Sync
Consolidating closed-form vision geometry, spatial decoupling, kernel diagnostics, and bug resolutions
1. Inverse Perspective Mapping • Closed-Form Flat-Earth Raycasting: Inverts pinhole projection (Z_road=0) solving (X_v, Y_v) at 50+ FPS on standard CPU without neural depth models. • Dual 3D Bounding Geometry: nuScenes class priors vs. camera-derived optical spans; boxes anchored to ground surface (Z=H/2). • Non-Destructive MCAP Enrichment: Injects /vision/geo_tracks in Electric Magenta with 0.0ms timestamp delta and byte-for-byte log preservation. • Radar-Vision Hungarian Association: Automated bipartite matching (lapjv) with 3.5m gating, computing near/mid/far MAE and RMSE.
2. Spatial Decoupling & Sync • IMU-Assisted Auto-Leveling: 1-tap gravity pitch extraction (GAME_ROTATION_VECTOR), digital clamp spirit level (±0.8°), and ADAS quality badge. • Camera / Radar Boresight Decoupling: Separates Camera Heading (0.0°) from Bumper Radar Squint (+1.0°), eliminating 17px vision track lateral drift. • Master Timeline Synchronizer: Hardware sequence mapping eliminates 2.16s video phase lead (Bug #22); adds /sync/frame_info. • 100 Hz Zero-Jitter Kinematics: SPSC lock-free ring buffer and SENSOR_DELAY_FASTEST bypass HAL filters, locking to native 104 Hz.
3. Deep-Tech Toolchain & Hardening • On-Device Perfetto Kernel Tracing: Zero-overhead scheduler & IRQ tracing via ADB shell; proves <0.05ms app slice execution. • Standalone Interactive HTML Reports: Zero-dependency offline single-file report (~1.2MB) with mouse-locked HUD and 6-panel lockstep zooming. • 10,400 FPS MCAP Pipeline: 80x throughput boost converting 40-minute driving sessions in 33 seconds via O(log N) binary search. • Central Web Dashboard (:8088): 1-click runner orchestrating sync audit, MCAP build, 8-point health checks, and geometric vision.
CRITICAL SYSTEM HARDENING COMPLETED: Root cause post-mortems conducted and permanently resolved for Bug #16 (MP4 moov Overflow), Bug #17 (TLV 6 FCW Decoding Offset), Bug #18 (Foxglove Schema Hash), Bug #19 (100 Hz IMU Jitter Spikes), Bug #21 (Pre-Roll Video Desync), Bug #22 (2.16s Video Phase Lead), Bug #23 (10,400 FPS Converter Boost), Bug #24 (Optical Pitch Sign Correction), and Bug #25 (Camera/Radar Yaw Decoupling).

## Slide 3
Inverse Perspective Mapping (IPM): Mathematical Derivation
Closed-form flat-earth raycasting (Z_road = 0) recovering 3D metric coordinates from 2D pixel contact patches
1. Inverse Optical Ray Back-Projection: Given 2D pixel coordinate [u, v, 1]^T and intrinsic matrix K, the normalized optical ray vector in camera frame {C} is: d_C = K^(-1) · [u, v, 1]^T = [(u - c_x)/f_x, (v - c_y)/f_y, 1]^T 2. Total Depression Angle (β): Taking the bottom-most bounding box edge (u_center, v_bottom) as the tire contact patch with road asphalt, the vertical optical ray angle combines camera mounting downward pitch (θ_mount) and vertical pixel deviation: β = θ_mount + arctan((v_bottom - c_y) / f_y) 3. Closed-Form Metric Ground Coordinates (Z_road = 0): Intersecting the line of sight with the flat road surface at camera height H_cam yields metric forward depth (Y_v) and lateral offset (X_v): Y_v = H_cam / tan(β) X_v = Y_v · ((u_center - c_x) / f_x) · cos(θ_mount) + ΔX • Invariant Property: The solution executes in O(1) constant time (<0.02 ms/target) with zero iterative root-finding, eliminating need for neural depth inference.
[ NATIVE EQUATION: Y_V = H / TAN(Β), X_V = Y_V · (U - CX)/FX ]
[ GEOMETRY DIAGRAM SLOT ] IPM Ground-Plane Raycasting Geometry Raycasting Schematic (Side & Top View):
• Optical center at height H_cam (1.35m)
• Downward pitch angle θ_mount (5.42°)
• Line of sight ray passing through pixel v_bottom
• Intersection with road asphalt plane (Z_road = 0)
• Recovery of longitudinal metric distance Y_v
• Lateral metric displacement X_v along camera HFOV

## Slide 4
IPM in Automotive ADAS: Decades of Heritage, Advantages & Pitfalls
Why ground-plane projection powers automotive ADAS, and where its physical assumptions break down
1. 30-Year Automotive ADAS Heritage: • Inverse Perspective Mapping was pioneered by Dickmanns (1988) and Bertozzi (1998) for autonomous highway driving (Prometheus project). • Core industrial foundation of commercial Lane Departure Warning (LDW) and front obstacle bounding systems (e.g. early MobilEye EyeQ chipsets). 2. Key Operational Advantages: • Ultra-Low Compute (O(1)): Requires only 3 trigonometric ops per target; operates at 50+ FPS on resource-constrained embedded edge processors without GPU acceleration. • Zero Neural Depth Hallucination: Monocular neural depth models (e.g. Depth Anything) suffer from scale ambiguity and heavy inference latency (~40-80ms). IPM is deterministic. • Metric Calibration Synergy: Directly consumes physical camera mount extrinsics [R | T] and pinhole intrinsics K.
3. Physical Vulnerabilities & Sensitivities: • Non-Flat Road Topology & Slopes (Z_road ≠ 0): Assumes a planar world. Uphill grades cause ray to strike earlier (distance over-estimation); downhill slopes delay intersection (under-estimation). • Dynamic Chassis Pitch Dynamics: Severe braking causes front chassis dive (-1.2°); hard acceleration causes rear squat (+1.5°). Uncompensated pitch distorts longitudinal range. • High-Range Pitch Sensitivity Divergence: Differentiating depth w.r.t pitch angle reveals quadratic error growth: ∂Y / ∂θ ≈ - (Y² / H_cam) At Y = 50m and H = 1.35m, a mere 0.5° pitch calibration error introduces a massive 16.2m longitudinal distance error! • Horizon Singularity: As v_bottom approaches the optical horizon (v -> v_horizon), tan(β) -> 0 and depth diverges to infinity.
[ NATIVE EQUATION: ∂Y / ∂Θ ≈ - (Y² / H_CAM) ]

## Slide 5
Modular Geometric Vision Pipeline & MCAP Integration
High-rate YOLO26 tracking, dual 3D bounding geometry, and non-destructive Foxglove topic injection
1. Modular Tracking & Orientation Engine: • Ultralytics YOLO26 + ByteTrack: Runs detection and multi-object tracking across vehicles, 2-wheelers, and pedestrians at 50+ FPS. • MP4 180° Inversion Handler: Parses container moov/tkhd matrix atoms, auto-rotating upside-down smartphone footage upright prior to inference. 2. Dual 3D Bounding Box Geometry: • Option A (Class Priors): Applies standardized automotive extents (Car: 1.8m x 1.5m x 4.2m, Pedestrian: 0.6m x 1.7m x 0.6m). • Option B (Camera-Derived Spans): Derives physical width and height directly from 2D pixel span: W_metric = (w_px / f_x) · Z_c, H_metric = (h_px / f_y) · Z_c • Road Elevation Anchor: Box center is elevated to Z = H / 2, ensuring 3D cuboids rest naturally on the road surface rather than buried. 3. Non-Destructive MCAP Topic Injection: • Streams 3D vision cuboids to Foxglove topic /vision/geo_tracks styled in Electric Magenta (rgba: 0.85, 0.10, 0.95, 0.75). • 100% Data Integrity: Preserves all 12 source channels and layout attachments byte-for-byte; source logs remain read-only.
[ FOXGLOVE 3D VIDEO SLOT ] Foxglove Studio 3D Perception Overlay Multi-Modal Perception Visualization:
• Upright 1080p camera feed in Camera View panel
• Cyan / Amber / Red TI mmWave radar tracks & Doppler vectors
• Electric Magenta (/vision/geo_tracks) 3D vision cuboids
• Billboard text labels showing ID, class, and metric range
• Perfect co-registration on vehicle targets with <0.04px error

## Slide 6
IMU-Assisted Camera Calibration & Live Horizon Engine
Eliminating pitch guesswork via gravity vector extraction, digital spirit level, and 25 Hz horizon follow
1. 1-Tap Gravitational Orientation Extraction: • Magnetic-Immune Telemetry: Leverages Sensor.TYPE_GAME_ROTATION_VECTOR (accel + gyro fusion), completely immune to EV motor and battery EMF distortion. • 1-Tap 'Sync Pitch' Button: Extracts physical mount pitch (θ = arcsin(R_8)) and roll (φ = arcsin(R_7)) in <10 ms, removing manual angle guesswork. 2. Digital Clamp Spirit Level & ADAS Quality Badge: • Digital Clamp Level: Displays glowing green indicator when phone is clamped within ±0.8° of road level; displays guidance arrows if tilted. • ADAS Pitch Quality Badge: Classifies windshield tilt into OPTIMAL (3°-12°), TOO SHALLOW (<3°), TOO STEEP (>12°), or FACING UP (<0°). 3. 25 Hz Live Horizon & Pillarbox Studio Layout: • Dynamic Horizon Follow: Projects artificial ground horizon line at 25 Hz tracking vehicle pitch/roll dynamics live on screen. [LOCK PITCH] seals the angle permanently into calibration JSON. • Natural Pillarbox Wings: Utilizes 19.5:9 display's 210px side pillarbox wings to host pitch/yaw controls, leaving central 16:9 preview 100% unoccluded.
[ ANDROID APP UI SLOT ] Fullscreen Calibration Studio UI RoadSense Android App Cockpit:
• Top bar: Digital Clamp Spirit Level pill (±0.8°)
• Pitch Quality Badge ('OPTIMAL PITCH 5.4°' in green)
• Central 16:9 camera preview with live artificial horizon line
• Left pillarbox wing: Camera Pitch (θ_cam) & 1-Tap Sync
• Right pillarbox wing: Isolated Radar Bumper Yaw (ψ_rad)
• Extrinsics Dialog for physical mount baseline entry

## Slide 7
Master Sensor Alignment: Decoupling Camera Boresight from Radar Squint
Eliminating cross-sensor distortion by establishing an explicit two-tier vehicle coordinate architecture
1. The Cross-Sensor Conflation Defect (Bug #25): • The Defect: In earlier iterations, calibration conflated relative radar-camera offset into a single ambiguous 'yawDeg' parameter. • The Impact: When adjusting the slider to compensate for a +1.0° front bumper radar bracket squint, downstream tooling rotated the camera_optical /tf frame by +1.0°, causing a 17-pixel lateral skew in 3D vision tracks! 2. The Two-Tier Sensor-to-Vehicle Architecture: • Tier 1: Sensor-to-Vehicle Boresight: Separately defines Camera Boresight (cameraYawDeg, cameraPitchDeg) and Radar Mounting Squint (radarSquintDeg) relative to vehicle base_link. • Tier 2: Cross-Sensor Alignment: Camera heading defaults to 0.0° (pointing straight ahead). Bumper bracket adjustments are attributed strictly to radarSquintDeg (+1.0°). 3. Master Frame Standard Alignment: • base_link: ISO 8855 FLU (+X Forward, +Y Left, +Z Up) • radar_link: TI Native RFU (+X Right, +Y Forward, +Z Up) • camera_optical: OpenCV RDF (+X Right, +Y Down, +Z Optical Forward)
Target Frame | +X Axis | +Y Axis | +Z Axis
Vehicle (base_link) | Forward | Left | Up
Radar (radar_link) | Right | Forward | Up
Camera (camera_optical) | Right | Down | Forward (Depth)
[ DECOUPLING DIAGRAM SLOT ] Sensor Boresight vs. Squint Alignment Diagram Schematic Overview:
• Centerline vehicle driving axis (+X_base)
• Camera optical axis mounted straight ahead (ψ_cam = 0.0°)
• TI mmWave radar bumper bracket squint (ψ_radar = +1.0°)
• Independent coordinate transforms into unified base_link
• Zero frustum tilt on video overlays and 3D cuboids

## Slide 8
Radar-to-Vision Track Association & Spatio-Temporal Evaluation
Automated Hungarian bipartite matching and distance-binned error metrics against mmWave radar ground truth
1. Spatio-Temporal Association Engine: • Temporal Matching Window: Matches /vision/geo_tracks with /radar/tracks within a strict ±50 ms temporal gate using master UTC nanosecond timestamps. • Hungarian Bipartite Assignment: Constructs a 2D Euclidean distance cost matrix on the ground plane, solved via Jonker-Volgenant algorithm (lap.lapjv). • Spatial Gating Cutoff: Enforces a 3.5-meter distance threshold to prevent false associations with roadside clutter or adjacent lane vehicles. 2. Distance-Binned Quantitative Metrics: • Performance is segmented into 3 operational distance zones: - Near-Field (0-15m): High optical pixel resolution, maximum tracking accuracy. - Mid-Range (15-30m): Nominal ADAS braking horizon; balanced radar/vision. - Far-Field (>30m): IPM pitch sensitivity begins to dominate; radar range truth. • Computed Statistics: Longitudinal MAE/RMSE (ΔY), Lateral MAE/RMSE (ΔX), 2D spatial error, and overall track association percentage. • Automated Evaluation CLI: evaluate_vision_vs_radar.py generates machine-readable benchmark reports (benchmark_report.json) for fleet validation.
[ BENCHMARKING CHART SLOT ] Radar vs. Vision Ground-Plane Track Association Map Benchmarking Visualization:
• Ground-plane scatter plot (X_v, Y_v) comparing sensors
• Blue points: Vision IPM ground contacts
• Red points: mmWave radar track centroids
• Green lines: Hungarian association correspondences
• Zone breakdown cards: Near / Mid / Far RMSE
• Cumulative association match rate scorecard

## Slide 9
Master Timeline Synchronizer: Nanosecond Multi-Sensor Alignment
Resolving cumulative video phase lead (Bug #22) via hardware-sequence locking and linear interpolation
1. The 2.16-Second Video Phase Lead (Bug #22): • The Symptom: In a 40-minute driving session, camera video moved 2.16 seconds before wheel speed, IMU acceleration, or radar tracks climbed. • Root Cause: Hardware MediaRecorder captured 72,336 packets with 0 drops, while userspace dropped 91 shutter callbacks under CPU load. Sequential row indexing shifted later video packets 2.16s into the past! 2. The Hardware Sequence Mapping Invariant: • Hardware Camera Counter: CaptureResult.getFrameNumber() strictly increments by 1 for every exposure. The invariant: expected_hw_seq = video_start_seq_id + packet_idx holds with 100% precision across entire sessions regardless of dropped userspace callbacks. 3. Linear Interpolation & /sync/frame_info Channel: • When a callback is dropped, master_timeline_synchronizer.py interpolates its timestamp using the camera crystal clock (33.293 ms/frame). • Integrated Channel: Injects /sync/frame_info into MCAP, stamping each frame with its matched radar frame ID and nanosecond delta (<15ms).
[ TIMING SYNCHRONIZATION GRAPH SLOT ] Nanosecond Timeline Alignment Verification Plot Cross-Sensor Timing Correlation Graph:
• Blue trace: Vehicle video presentation timestamp (PTS)
• Red trace: TI mmWave radar frame arrival timestamps
• Green trace: CAN wheel speed climb during acceleration
• Phase lead verification: Zero drift across 40-minute drive
• Verified sync delta: <14.88 ms at t = 720.96s (radar frame 21,032)

## Slide 10
100 Hz Zero-Jitter Kinematics Subsystem & Android OS Hardening
Bypassing Android HAL decimation filters to achieve sub-millisecond IMU jitter at native 104 Hz
1. The 18 ms Jitter Spike Elimination (Bug #19): • The Quirk: Requesting explicit microsecond periods (e.g. 10,000 µs) activated Android HAL software decimation, creating periodic 18 ms jumps (Δt_prev + Δt_spike = 30.0 ms). • The Solution: Switched to SENSOR_DELAY_FASTEST (0 µs) with an SPSC lock-free ring buffer, locking to ST LSM6DSL native 104 Hz rate with sub-millisecond jitter (σ < 1.0 ms). 2. Real-Time Gravity-Free Linear Acceleration: • Sensor.TYPE_LINEAR_ACCELERATION: Continuously separates and removes Earth gravity (9.81 m/s²) from total acceleration in real time on the phone. • Clean Dynamics: Provides pure dynamic braking and cornering forces without tilt bias. 3. Magnetic-Immune 6-DOF Game Rotation Vector: • Derives orientation quaternion (x,y,z,w) using solely accelerometer and gyro integration, ignoring the magnetic compass. • EV Hardening: Guarantees heading stability around high-voltage EV motor inverters and heavy electrical wiring harnesses.
[ IMU KINEMATICS CHART SLOT ] 100 Hz IMU Jitter Distribution & Kinematics Acceleration Curves Kinematics Telemetry Plots:
• Inter-frame interval histogram centered at 9.615 ms (104 Hz)
• Jitter distribution showing σ < 0.99 ms and zero 18 ms spikes
• Linear acceleration curves during aggressive vehicle braking
• Game rotation vector Euler angles (Pitch, Roll, Yaw)
• Microsecond monotonic timestamp alignment with video

## Slide 11
Deep-Tech Diagnostics: On-Device Perfetto Kernel Tracing via ADB
Zero-overhead nanosecond Linux kernel scheduler and hardware IRQ profiling on target hardware
1. The Zero-Overhead Tracing Architecture: • The Diagnostic Dilemma: Evaluating microsecond timing anomalies with userspace loggers introduces CPU overhead, altering system behavior (Heisenberg effect). • The Perfetto Toolchain: Scripts (record_perfetto_trace.py & analyze_perfetto_trace.py) configure Android's kernel-level ftrace daemon via ADB shell with a 32-64MB circular buffer (<1% CPU impact) on unrooted hardware. 2. Tracked Subsystems & Application Slices: • Linux CFS Scheduler: sched/sched_switch, sched_wakeup, and big.LITTLE core migration. • Hardware Interrupts: irq/irq_handler_entry and exit tracking ST LSM6DSL physical interrupts. • Custom App Trace Slices: High-precision Trace.beginSection('RoadSense:onSensorChanged') markers. 3. Definitive Diagnostic Finding: • Proved that RoadSense-ImuThread processes samples in <0.05 ms with zero CPU starvation. • Conclusively demonstrated that 18 ms spikes originated from vendor HAL software decimation rather than OS scheduling delays.
[ PERFETTO UI TRACE SLOT ] Perfetto System Trace Visualization (ui.perfetto.dev) Kernel Scheduler Trace Breakdown:
• CPU 0-7 big.LITTLE scheduling swimlanes
• RoadSense-ImuThread execution slices (<0.05 ms)
• ST LSM6DSL hardware IRQ arrival pulses
• Thread state timeline: Running vs. Runnable vs. Sleeping
• Nanosecond correlation with imu_frames.csv ticks

## Slide 12
Data Delivery: Standalone Interactive HTML Audit Reports & HUD
Zero-dependency offline inspection reports with synchronized 6-track zooming and jitter-free crosshair HUD
1. Zero-Dependency Standalone Architecture: • Solves Matplotlib Squish: Static PNGs squished nominal 20 ms data into flat lines due to 500 ms camera startup spikes. HTML reports provide dynamic zooming. • Completely Offline (~1.2 MB): Inlines Plotly.js directly. Opens on any PC via file:/// without Python, internet, or local servers. 2. Foxglove-Style Mouse-Locked HUD: • The Innovation (Bug #20): Standard Plotly tooltips violently jumped 80px vertically when hovering noisy 100 Hz signals. We decoupled tooltips from discrete points, locking a vertical crosshair to cursor clientX with O(log N) binary search. • Result: Completely jitter-free hover readout across all 6 sensor tracks. 3. Sticky Navigation & Dual Certification Scorecards: • 1-Click View Toggles: Sticky toolbar with 'Steady-State Focus', 'Show All Spikes', 'Startup Phase (0-5s)', and 'Teardown Phase'. • Dual Scorecards: Side-by-side 8-Point Subsystem Health + 10-Point Cross-Sensor Sync verification table with CERTIFIED GOLD badges.
[ INTERACTIVE HTML REPORT SLOT ] Interactive Multi-Sensor HTML Audit Dashboard HTML Audit Report UI (Plotly.js):
• Coordinated 6-panel synchronized time series
• Sticky navigation bar with 1-click view toggles
• Foxglove-style mouse-locked vertical crosshair HUD
• Zooming on one panel zooms all 6 tracks in lockstep
• Executive Summary card with CERTIFIED GOLD certification
• Complete 10-point cross-sensor sync audit checklist

## Slide 13
Central Web Dashboard: Single Unified Script Execution Platform
Zero-dependency local cockpit on :8088 running synchronization, conversion, health audits, and vision
1. Zero-Dependency Local Web Server (:8088): • Built using Python's standard http.server with Server-Sent Events (SSE) live streaming. • Zero external web framework dependencies (no Flask/Django/Node.js required for desktop analytics). • Live ADB monitoring: Connected device serial, battery level, storage space, and session discovery. 2. 1-Click Multi-Script Runner Pipeline: • Single Unified Cockpit: Replaces fragmented manual terminal commands with an automated 1-click execution pipeline: Raw Session Ingestion ──► Master Timeline Sync ──► 10,400 FPS MCAP Build ──► 8-Point Health Audit ──► Geometric Vision Ingestion • Real-Time Progress: Streams console stdout/stderr live to browser terminal. 3. Native OS & Artifact Integration: • Native /api/open_folder: Opens Windows Explorer directly to session logs in 1 click. • Direct HTML Report Links: Launches interactive Plotly audit dashboards instantly.
[ WEB COCKPIT UI SLOT ] RoadSense Central Web Dashboard Cockpit (:8088) Web Cockpit Interface Overview:
• Dark-mode responsive automotive dashboard
• ADB device health badge (Samsung Galaxy M30)
• Session archive table with sensor availability tags
• 1-Click 'Run All Audits' master action banner
• Live Server-Sent Events (SSE) execution log modal
• Direct 'Open Folder' and 'View Report' actions

## Slide 14
Root Cause Analysis: Subsystem Hardening Post-Mortems (Part 1)
Eliminating container metadata overflows, CAN telemetry shifts, schema rejections, and IMU jitter
Bug #16: Large MP4 Metadata Overflow • Symptom: Recordings >500MB crashed MCAP video parser with 'moov atom not found'. • Root Cause: Parser used fixed 64KB tail buffer; moov atom scales with duration, growing to 2-8MB in long drives. • Solution: Implemented ISO box traversal jumping directly to moov header via box length offsets in O(1) zero-copy time.
Bug #17: 1-Byte Offset in TLV 6 FCW Telemetry • Symptom: Forward Collision Warning (FCW) target coordinates were severely misreported as TargetX. • Root Cause: Firmware packed a 1-byte counter before CAN payload, shifting bitfield decoding by 8 bits. • Solution: Corrected decoding byte offset and integrated color-coded FCW alerting (Green/Amber/Crimson) in Foxglove.
Bug #18: Foxglove Anonymous Schema Hash • Symptom: Foxglove Studio rejected custom TypeScript calibration overlays with anonymous hash (0bb4508b). • Root Cause: Returning standard JavaScript number[] arrays or generic types broke Protobuf schema resolution. • Solution: Imported official @foxglove/schemas and instantiated typed Float64Array matrix buffers.
Bug #19: 100 Hz IMU 18 ms Jitter Spikes • Symptom: IMU logging had periodic 18 ms timestamp jumps every ~1.0s (Δt_prev + Δt_spike = 30.0 ms). • Root Cause: Explicit microsecond delays (10,000 µs) activated Android HAL software decimation filters. • Solution: Enforced SENSOR_DELAY_FASTEST (0 µs) with SPSC lock-free ring buffer, locking to ST LSM6DSL 104 Hz (σ < 1.0 ms).
Bug #20: Multi-Track Hover Tooltip Jitter • Symptom: Hovering over noisy 100 Hz signals caused tooltips to violently bounce 80px vertically. • Root Cause: Plotly default anchored tooltips to discrete (x,y) points rather than client cursor coordinates. • Solution: Decoupled HUD from discrete points; locked vertical crosshair to cursor clientX with O(log N) binary search.
Bug #21: Pre-Roll Shutter Video Desync • Symptom: Video frames drifted 900 ms out of phase with radar point clouds during replay. • Root Cause: Converters assumed MP4 packet 0 strictly mapped to CSV row 0, bypassing camera preview startup. • Solution: Structured synchronizer to ingest session_timeline.csv as ground truth, anchoring to record sequence start.

## Slide 15
Root Cause Analysis: Subsystem Hardening Post-Mortems (Part 2)
Eliminating video lead, converter bottlenecks, optical inversions, and cross-sensor conflation
Bug #22: 2.16s Video Lead via Dropped Callbacks • Symptom: Camera video led wheel speed and radar points by 2.16s in 40-minute driving sessions. • Root Cause: Android userspace dropped 91 callbacks under load, shifting sequential index mapping into the past. • Solution: MasterTimelineSynchronizer locks MP4 packets to hardware camera exposure IDs (S_start + idx); sync error < 15ms.
Bug #23: MCAP Converter Speed Collapse • Symptom: Conversion speed collapsed from >3,000 FPS to ~120 FPS with 0% GPU and <8% CPU load. • Root Cause: Uncached list comprehensions in frame lookups created 12.16B temporary Python objects, stalling GIL in GC. • Solution: Precomputed contiguous numpy arrays and O(log N) bisect lookups; throughput surged to 10,411 FPS (80x speedup).
Bug #24: Optical Pitch Sign Inversion (Rx(-P)) • Symptom: 3D radar bounding boxes in Foxglove floated ~180-190px too high into the sky above road vehicles. • Root Cause: Python tooling wrote Rx with inverted signs (Rx(-P) transpose), pointing optical axis +5.4° UP instead of DOWN. • Solution: Corrected Rx rotation signs in compute_camera_optical_tf; overlays land natively on vehicles with zero user scripts.
Bug #25: Camera Yaw Decoupling from Radar Squint • Symptom: Compensating for radar mounting squint tilted camera optical frustum, skewing vision tracks by 17px. • Root Cause: Calibration parameters conflated sensor-to-vehicle angles with relative cross-sensor offsets into single yawDeg. • Solution: Established two-tier architecture: cameraYawDeg (0.0°) vs radarSquintDeg (+1.0°); verified zero cross-distortion.
Bug #12: Exynos Dual-Stream HAL Stalling • Symptom: Camera2 HAL deadlock and ANR crashes when activating dual analysis streams on Samsung Exynos. • Root Cause: Hardware ISP enforces strict concurrent surface output limits, starving ImageReader buffers. • Solution: Road AE samples downsampled 32x24 bitmaps directly from active TextureView on Dispatchers.Default; zero extra streams.
Bug #13 & #14: Foxglove Ghosting & Seek Freeze • Symptom: Past radar tracks persisted indefinitely on 3D canvas; video seek froze on blank screens. • Root Cause: Dynamic entity IDs per frame caused object accumulation; sparse keyframes lacked closed GOPs. • Solution: Static entity ID 'radar_tracks' for atomic updates; enforced 1-sec closed GOP 30 (-forced-idr 1) in transcoding.

## Slide 16
Milestone Handover & System Perfection Roadmap
Consolidating Sprint 3 perception foundations and establishing disciplined hardware alignment targets
Sprint 3 Deliverables: 100% Complete Perception, Spatial Decoupling & Toolchain Foundation 1. Inverse Perspective Mapping (IPM) Operational [✔]: Closed-form flat-earth raycasting (50+ FPS) and non-destructive Foxglove MCAP topic injection (/vision/geo_tracks). 2. IMU-Assisted Camera Calibration Operational [✔]: 1-tap gravity pitch sync, digital clamp spirit level (±0.8°), ADAS quality badge, and 25 Hz live horizon tracking. 3. Master Sensor Decoupling Verified [✔]: Two-tier architecture separating Camera Boresight from Radar Squint; Bug #25 lateral drift resolved. 4. Master Timeline Synchronizer Active [✔]: Hardware camera sequence locking eliminates 2.16s video lead (Bug #22); /sync/frame_info stream active. 5. Deep-Tech Diagnostics Suite Operational [✔]: On-device Perfetto kernel tracing (<0.05ms app slice), offline interactive HTML reports, and 10,400 FPS converter. 6. System Hardening Complete [✔]: Bugs #11 through #25 diagnosed and permanently eliminated; 53 JVM unit tests passing clean.
Upcoming Priority: System Perfection Hardware Rigidity & Association Gates 1. The Current Physical Challenge: Experimental vehicle mounts currently exhibit minor bracket vibration and mechanical pitch/yaw play during road tests, introducing dynamic sensor alignment variance. 2. Hardware Mount Hardening: • Fabricate rigidized mechanical mounting brackets for front bumper radar. • Implement vibration-damped windshield smartphone mount. • Perform static ground-truth extrinsic survey on certified level ground. 3. The Strict Quantitative Association Gate: • Target Milestone: Achieve sustained > 66% radar-vision track association across continuous drive cycles. • Disciplined Strategy: Advance to supervised model training and automated validation only AFTER the 66% physical association gate is reliably breached.
Questions & Technical Discussion